# 14. ACCELERATED STALL

PREFORMED BY: 								DATE:

Temperature:			Wind Speed:			Direction:		Duration:

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight |  |
| 2 | Perform preflight inspection according to the checklist as well as: Check the TORQUE (paint marks) on the engine mounts, propeller bolts and landing gear. Double check the flight control hinges and rod end bearings for attachment and play. Check all cable installations, cable tension, and control travel Check the oil and fuel filters for metal or other forms of contamination. |  |
| 3 | Taxi to test runway monitoring all instruments and gauges |  |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway ______________ for local flying |  |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! |  |
| 6 | BEST ANGLE OF CLIMB: 45 Knots BEST GLIDE SPEED: 45 Knots MANEUVERING SPEED: 60 Knots |  |
| 7 | Accelerated stall: It is an in-flight stall at more than one g, similar to what is experienced in a steep turn or a pull up. The two standard methods for accelerated stalls are the constant g (constant bank) and constant speed (increasing bank). Most preferred of the two is the constant bank method in which the airspeed characteristics of the aircraft is decreased and the angle of bank is held constant, until the aircraft stalls. It is the most preferred because the potential violence of any accelerated stall is largely governed by the increasing g load and air-speed. Start with small bank angles -- 30 degrees will produce 1.15 g. Decelerate slowly, ball in the center, do not over control. Work up incrementally to a two g, 60 degree bank. The pilot needs only to record the airspeed and bank angle in which the aircraft hits the pre-stall buffet. Recover by adding power and reducing the angle of bank. Airspeed: Bank Angle: Recover by adding power and reducing the angle of bank |  |
| 8 | Perform a carbon monoxide (CO) test using an industrial CO test meter |  |
| 9 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway _______________ |  |
| 10 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway _______________, full stop |  |
| 11 | Taxi to hanger and carryout a complete inspection of the aircraft |  |

### Comments: