# 1. AIRCRAFT CHECK

PREFORMED BY: 	Alistar Hall Level 2 - LAME		      DATE: 12 September 2002

| S = Satisfactory U = Unsatisfactory | Satisfactory |
| --- | --- |
| Registration/Airworthiness/Operation Limits | S |
| Aircraft Identification Plates Installed | S |
| Amateur Built Placard Installed | S |
| Weight and Balance/Equipment List | S |
| WINGS |
| Remove Inspection Plates/Fairings | S |
| General Inspection of Exterior/Interior Wing | S |
| Flight Controls proper Attachment (No Slop) | S |
| Flight Control Hinges/Rod End Bearings Serviceability | S |
| Flight Controls properly Rigged/Proper Tension | S |
| Inspect all Control Stops for Security | S |
| Trim Control Surface/Hinges/Rod End bearing Service | S |
| Propped Rivets/Cracked/Deformed Skin | S |
| Lubrication | S |
| Wing Attach Points | S |
| Flying/Landing Wires/Struts for Security | S |
| Corrosion | S |
| Flight Control Bolts/Pins for Safety and Condition | S |
| Wing/Strut/Cable attachments and Hardware for Safety and Condition | S |
| FUEL SYSTEM |  |
| Corrosion | S |
| Fuel Lines for Chafing/leaks/Security/Condition | S |
| Sump all Fuel Tanks for Water or Debris | S |
| Fuel Caps for Security | S |
| Fuel Placard (For and Special/Uncommon Requirements) | S |
| Fuel Valve/Cross Feed/for operation and Security | S |
| Clean Fuel Filters/Gasolator/Flush System | S |
| Inspect Fuel Tank Vent System | S |
| LANDING GEAR |  |
| Inspect Struts/Torque Links for Attachments | S |
| Inspect Struts for Proper Extension | S |
| Inspect for Hydraulic Leaks | S |
| Check all Bushings for Wear/Free Play | S |
| Check Lubrication | S |
| Inspect Wheels for Alignment | S |
| Wheel Tyres for Cracks and Serviceability | S |
| Wheel Bearings for Lubrication | S |
| Inspect for Corrosion | S |
| Inspect Nose Gear for Cracks and Travel | S |
| Check Tyre Pressure | S |
| Brake Lining within Limits | S |
| Brake Discs for Cracks, Wear and Deformity | S |
| Brake Hydraulic Lines for leaks and Security | S |
| FUSELAGE |  |
| Remove Inspection Plates and Panels | S |
| Inspect Bulkheads and Stringers for Popped Rivets and Cracked Skin | S |
| Inspect the Security of all Internal Lines | S |
| Inspect Windows/Canopy for Cracks and Fit | S |
| Inspect Door or Canopy Latching Mechanism | S |
| Inspect Fire Wall for Distortion and Cracks | S |
| Check Control Stick/Yoke for Freedom of Movement | S |
| Check Control and Pulleys for Attachment and Operation | S |
| Ensure Cockpit Instruments are Properly Marked | S |
| Inspect Instruments, Lines for Security | S |
| Inspect Cockpit Fresh Air Vents/Heater Vents for Operation and Security | S |
| Inspect Seats, Seat Belts/Shoulder Harness for Security and Attachment | S |
| Corrosion | S |
| EMPENNAGE/CANARD |  |
| Remove Inspection plates and Fairings | S |
| Inspect Vertical Finn Attach Points | S |
| Inspect Elevator/Stabiliser Attach Points | S |
| Inspect Hinges/Trim Tabs/Rod Ends for Attachment and Free Play (Slop) | S |
| Inspect Empennage/Canard Skin for Damage/Corrosion | S |
| Inspect all Control cables, Hinges and Pulleys | S |
| Inspect all Control Stops | S |
| Check all Attachment Points and Controls for Safety Condition | S |
| Check Safeties on Exhaust Springs | S |
| PROPELLER |  |
| Check Spinner and Back Plate for Cracks | S |
| Inspect for Cracks/Stone Damage/Nicks | S |
| Check for Delamination (Wood/Composite Blades) | S |
| Check Prop Bolts Torque/Safety Wire | S |
| Check for Oil Leaks (Crankcase Nose Seal) | S |
| Check Prop Track | S |
| Check Prop Balance (Wood Prop – at engine run up test) | S |
| Electrical | S |
| Spare Fuses Available | S |
| Battery Serviced and Free from Corrosion | S |
| Battery Box Free from Corrosion | S |
| Check Anti Collision Light for Operation | S |
| Inspect all Antenna Mounts and Wiring for Security | S |
| Inspect Radios/Leads/Wires for Attachment and Security | S |
| Inspect Circuit breaker/Fuses/Panes for Condition | S |
| OPERATION INSPECTION: |  |
| Visual Inspection of the Engine/Propeller | S |
| All Inspection Panels and fairings Secure | S |
| Proper Fuel in Tanks | S |
| Engine Start Procedures – Engine to be run at full power for 3 minutes continuously | S |
| Oil Pressure/Oil Temperature within Limits | S |
| Magneto Check/Hot Mag Check | S |
| Idle RPM/Mixture Check | S |
| Static RPM Check | S |
| Electrical System Check | S |
| Cool Down Period/Engine Shut Down | S |
| Perform Oil Hydraulic and Fuel Leak Check | S |
| PAPERWORK |  |
| Airworthiness Directives | S |
| Record Findings and Sign Off Inspection | S |
| Maintenance in Aircraft Log Books | S |