# 8. AIRSPEED ACCURACY

PREFORMED BY: 	Tony Stiller					DATE: 19 May 2003

Temperature:	 30C	  Wind Speed:   15-20 Knots	       Direction: N-West         Duration: 1.3hrs

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight | ( |
| 2 | Perform preflight inspection according to the checklist | ( |
| 3 | Taxi to test runway monitoring all instruments and gauges | ( |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway 30 for local flying |  |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! | ( |
| 6 | BEST ANGLE OF CLIMB: 50 Knots BEST GLIDE SPEED: 50 Knots MANEUVERING SPEED: 50 Knots | ( |
| 7 | Airspeed Accuracy Test: fly a precision course maintaining a constant altitude (e.g., 1,000 feet), constant airspeed, constant magnetic heading, and constant engine rpm. The pilot must record the temperature, altitude, indicated airspeed and the time over each landmark for both directions. The average of these speeds is the ground speed of the aircraft. Record all the data in order to prepare an airspeed calibration table for the flight manual. Engine Rpm Heading GPS mph Conversion Knots Air Speed Indicator Knots Difference Knots Altitude feet GPS 2400 80 92 80 64 -16 2000 2400 340 54 47 66 +19 2000 2400 160 105 91 65 -27 2000 2400 260 53 46 65 +19 2000 Instruments Readings CHT 150 Oil Temp. 90 Oil Pressure Kpa x 100 2.5 Volts 14 Comments: Based on these results it will be best to rely on the GPS readings. |  |
| 8 | Perform a carbon monoxide (CO) test using an industrial CO test meter | ( |
| 9 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway 30 | ( |
| 10 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway 30, full stop | ( |
| 11 | Taxi to hanger and carryout a complete inspection of the aircraft | ( |