# 10. BEST RATE OF CLIMB

PREFORMED BY: 	Tony Stiller					    DATE: 10 May 2003

Temperature:	 22C	     Wind Speed: 5 - 10 Knots      Direction: S-SE          Duration: 1.3Hrs

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight | ( |
| 2 | Perform preflight inspection according to the checklist as well as: Check the TORQUE (paint marks) on the engine mounts, propeller bolts and landing gear. Double check the flight control hinges and rod end bearings for attachment and play. Check all cable installations, cable tension, and control travel Check the oil and fuel filters for metal or other forms of contamination. | ( |
| 3 | Taxi to test runway monitoring all instruments and gauges | ( |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway 12 for local flying | ( |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! | ( |
| 6 | BEST ANGLE OF CLIMB: 50 Knots BEST GLIDE SPEED: 50 Knots MANEUVERING SPEED: 50 Knots |  |
| 7 | Best Rate of Climb Speed Tests. Perform the tests in smooth air, free from thermal activity. The airspeed that shows the greatest gain in altitude is the aircraft’s best rate of climb speed (Vy). Select a BASE altitude of 1,000 feet AGL. Use a heading 90 degrees to the wind Apply full throttle climb well below the predetermined BASE altitude and stabilise at 55 knots Begin a one minute time check. At the end of 1 minute record the altitude gained. = feet |  |
| 8 | Best Rate of Climb Speed Tests. Perform the tests in smooth air, free from thermal activity. Select a BASE altitude of 2,000 feet AGL. Use a heading 90 degrees to the wind Apply full throttle climb well below the predetermined BASE altitude and stabilise at 60 knots Begin a one minute time check. At the end of 1 minute record the altitude gained. = feet |  |
| 9 | Best Rate of Climb Speed Tests. Perform the tests in smooth air, free from thermal activity. Select a BASE altitude of 2,000 feet AGL. Use a heading 90 degrees to the wind Apply full throttle climb well below the predetermined BASE altitude and stabilise at 55 knots Begin a one minute time check. At the end of 1 minute record the altitude gained. = feet |  |
| 10 | Best Rate of Climb Speed Tests. Perform the tests in smooth air, free from thermal activity. Select a BASE altitude of 2,000 feet AGL. Use a heading 90 degrees to the wind Apply full throttle climb well below the predetermined BASE altitude and stabilise at 50 knots Begin a one minute time check. At the end of 1 minute record the altitude gained. = feet |  |
| 11 | Draw a graph feet per minute 0 10 20 30 40 50 60 70 Air speed in knots |  |
| 12 | Best Angle of Climb Speed Tests. Best angle of climb speed can be found by using the same chart developed for the best rate of climb tests. Draw a line (tangent) from the zero rate of climb feet per minute (above) outward to a point, on the rate of climb airspeed curve. Where both lines touch, draw a line straight down to the airspeed leg of the chart. The airspeed that the line intersects is the best angle of climb airspeed. |  |
| 13 | Perform a carbon monoxide (CO) test using an industrial CO test meter |  |
| 14 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway _______________ |  |
| 15 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway _______________, full stop |  |
| 16 | Taxi to hanger and carryout a complete inspection of the aircraft |  |

### Comments: