# 18. FUEL CONSUMPTION

PREFORMED BY: 	Tony Stiller						DATE: 10 May 2003

Temperature:	 25C		Wind Speed:	10-15 Knots  	Direction: SE		Duration: 2.7hrs

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight | ( |
| 2 | Perform preflight inspection according to the checklist as well as: Check the TORQUE (paint marks) on the engine mounts, propeller bolts and landing gear. Double check the flight control hinges and rod end bearings for attachment and play. Check all cable installations, cable tension, and control travel Check the oil and fuel filters for metal or other forms of contamination. | ( |
| 3 | Taxi to test runway monitoring all instruments and gauges | ( |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway 12 for local flying | ( |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! | ( |
| 6 | BEST ANGLE OF CLIMB: 50 Knots BEST GLIDE SPEED: 50 Knots MANEUVERING SPEED: 50 Knots |  |
| 7 | Fuel Consumption: a good indication of how much the engine is working for each rpm produced. For a new or recently overhauled engine, the fuel consumption should improve each flight hour until the engine finishes its ‘‘break in’’ period, i.e., after approximately 100 hours of operation. Lay out a race track course with 8 to 10 mile legs Determine the approximate fuel burn to reach 1500, 3000, 4500 feet of altitude. With full tanks, climb to 4500 feet and run the race track course for half an hour at 75% power. Comments: 17.4 litres per hour with a new engine with 22 hours run-time. | ( ( ( ( |
| 8 | Perform a carbon monoxide (CO) test using an industrial CO test meter | ( |
| 9 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway 12 | ( |
| 10 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway 12 full stop | ( |
| 11 | Taxi to hanger and carryout a complete inspection of the aircraft | ( |

### Comments:

The burn rate of 17.4 litres per hours is less than the 20 litres per hour specified in the Jabiru manual for the 3300 litre engine.