# 17. MAGNETIC COMPASS

PREFORMED BY: 	Tony Stiller					DATE: 19 May 2003

Temperature:	 30C	  Wind Speed:   15-20 Knots	       Direction: N-West         Duration: 1.3hrs

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight | ( |
| 2 | Perform preflight inspection according to the checklist as well as: Check the TORQUE (paint marks) on the engine mounts, propeller bolts and landing gear. Double check the flight control hinges and rod end bearings for attachment and play. Check all cable installations, cable tension, and control travel Check the oil and fuel filters for metal or other forms of contamination. | ( |
| 3 | Taxi to test runway monitoring all instruments and gauges | ( |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway 30 for local flying | ( |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! | ( |
| 6 | BEST ANGLE OF CLIMB: 50 Knots BEST GLIDE SPEED: 50 Knots MANEUVERING SPEED: 50 Knots | ( |
| 7 | The Magnetic Compass. The magnetic compass should have been checked for accuracy prior to the first flight. However, the addition and removal of equipment, changing of wire bundle routing, and other airframe modifications may have affected the accuracy of the instrument. Check compass setting against GPS readings when traveling in a straight line at cruise speed GPS Magnetic Compass 140 150 270 260 | ( |
| 8 | Perform a carbon monoxide (CO) test using an industrial CO test meter | ( |
| 9 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway 30 | ( |
| 10 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway 30, full stop | ( |
| 11 | Taxi to hanger and carryout a complete inspection of the aircraft | ( |

### Comments:

Consistent 10 degrees difference between GPS reading and magnetic compass.