# 16. MAXIMUM CEILING

PREFORMED BY: 								DATE:

Temperature:			Wind Speed:			Direction:		Duration:

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight |  |
| 2 | Perform preflight inspection according to the checklist as well as: Check the TORQUE (paint marks) on the engine mounts, propeller bolts and landing gear. Double check the flight control hinges and rod end bearings for attachment and play. Check all cable installations, cable tension, and control travel Check the oil and fuel filters for metal or other forms of contamination. |  |
| 3 | Taxi to test runway monitoring all instruments and gauges |  |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway ______________ for local flying |  |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! |  |
| 6 | BEST ANGLE OF CLIMB: 45 Knots BEST GLIDE SPEED: 45 Knots MANEUVERING SPEED: 60 Knots |  |
| 7 | Service ceiling: The climb to the aircraft service ceiling should be made in a series of step climbs during which engine performance, temperatures and pressures are recorded. At the slightest indication of engine performance or aircraft control problems, the pilot should terminate the test and return to the airport. |  |
| 8 | Perform a carbon monoxide (CO) test using an industrial CO test meter |  |
| 9 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway _______________ |  |
| 10 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway _______________, full stop |  |
| 11 | Taxi to hanger and carryout a complete inspection of the aircraft |  |

### Comments: