# 15. MAXIMUM GROSS WEIGHT

PREFORMED BY: 								DATE:

Temperature:			Wind Speed:			Direction:		Duration:

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight |  |
| 2 | Perform preflight inspection according to the checklist as well as: Check the TORQUE (paint marks) on the engine mounts, propeller bolts and landing gear. Double check the flight control hinges and rod end bearings for attachment and play. Check all cable installations, cable tension, and control travel Check the oil and fuel filters for metal or other forms of contamination. |  |
| 3 | Taxi to test runway monitoring all instruments and gauges |  |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway ______________ for local flying |  |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! |  |
| 6 | BEST ANGLE OF CLIMB: 45 Knots BEST GLIDE SPEED: 45 Knots MANEUVERING SPEED: 60 Knots |  |
| 7 | Maximum gross weight from stalls, rates of climb, angles of climb, stability, retraction tests, slow flight, through accelerated stalls should be investigated. Each phase of the testing should be done slowly, incrementally, with the same careful attention to detail that should characterize all the flight testing. weight should be done in a series of steps. Usually, 20 percent increments of the maximum payload (e.g., sandbags, lead shot) are added in the aircraft to simulate passengers or baggage weight. The pilot should carefully weigh and secure the ballast. A new weight and balance and CG location must be worked for each new increase in weight. Stop testing when the aircraft’s maximum gross weight is reached. |  |
| 8 | The maximum gross weight test results should be recorded in the flight manual. If there are any changes to the stall speed initially marked on the airspeed indicator, it should be changed to reflect the aircraft stall speed at maximum gross weight. Weight of Aircraft: Weight of Pilot: Quantity of Fuel: Weight of Fuel: Added Weigth: Maximum Weight: 544Kg |  |
| 9 | Perform a carbon monoxide (CO) test using an industrial CO test meter |  |
| 10 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway _______________ |  |
| 11 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway _______________, full stop |  |
| 12 | Taxi to hanger and carryout a complete inspection of the aircraft |  |

### Comments: