# 11. SLOW FLIGHT TEST

PREFORMED BY: 								DATE:

Temperature:			Wind Speed:			Direction:		Duration:

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight |  |
| 2 | Perform preflight inspection according to the checklist as well as: Check the TORQUE (paint marks) on the engine mounts, propeller bolts and landing gear. Double check the flight control hinges and rod end bearings for attachment and play. Check all cable installations, cable tension, and control travel Check the oil and fuel filters for metal or other forms of contamination. |  |
| 3 | Taxi to test runway monitoring all instruments and gauges |  |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway ______________ for local flying |  |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! |  |
| 6 | BEST ANGLE OF CLIMB: 45 Knots BEST GLIDE SPEED: 45 Knots MANEUVERING SPEED: 60 Knots |  |
| 7 | Slow Flight Test. For added safety, the slow flight tests should be performed at 6,000 AGL or higher to allow room for spin recovery. THE PRIMARY PURPOSE OF THESE TESTS IS FOR THE PILOT TO BECOME FAMILIAR WITH THE AIRCRAFT’S HANDLING QUALITIES AT THE MINIMUM GEAR UP/DOWN AIRSPEEDS AND POWER SETTINGS. AVOID BANK ANGLES OF MORE THAN 5 DEGREES. Start the tests at an airspeed of 1.3 times the stall speed of the aircraft. = 39 Knots Once the aircraft is stabilized and maintaining its altitude, reduce the airspeed by 5 knots Maintain the altitude Keep reducing the airspeed until approaching a stall. Maintain 5 knots above the previously determined stall speed = Knots |  |
| 8 | Perform a carbon monoxide (CO) test using an industrial CO test meter |  |
| 9 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway _______________ |  |
| 10 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway _______________, full stop |  |
| 11 | Taxi to hanger and carryout a complete inspection of the aircraft |  |

### Comments: