# 12. STATIC AND DYNAMIC       LONGITUDINAL STABILITY

PREFORMED BY: 								DATE:

Temperature:			Wind Speed:			Direction:		Duration:

| Step | Procedure | Satisfactory |
| --- | --- | --- |
| 1 | Correct discrepancies noted on the first flight |  |
| 2 | Perform preflight inspection according to the checklist as well as: Check the TORQUE (paint marks) on the engine mounts, propeller bolts and landing gear. Double check the flight control hinges and rod end bearings for attachment and play. Check all cable installations, cable tension, and control travel Check the oil and fuel filters for metal or other forms of contamination. |  |
| 3 | Taxi to test runway monitoring all instruments and gauges |  |
| 4 | Radio Call All stations Caboolture, this is BushCaddy 3670 departing runway ______________ for local flying |  |
| 5 | Accelerate to predicted rotation speed If the aircraft does not want to rotate or unusual stick forces are experienced, abort the takeoff! |  |
| 6 | BEST ANGLE OF CLIMB: 45 Knots BEST GLIDE SPEED: 45 Knots MANEUVERING SPEED: 60 Knots |  |
| 7 | An aircraft is said to be in a state of equilibrium when it experiences no acceleration and remains in a steady trimmed condition until the force or moment balance is disturbed by an atmospheric irregularity or by pilot input. Test for Static Longitudinal Stability. Climb to at least 6,000 feet AGL and trim the aircraft for zero stick force in straight and level flight at low cruising speed. Apply a light ‘‘pull’’ force and stabilize at an airspeed about 10 percent less than the trimmed cruise speed. At this reduced airspeed it should require a ‘‘pull’’ force to maintain the slower speed If it requires a ‘‘pull’’ force, pull a little further back on the stick and stabilize the airspeed at approximately 20 percent below the initial cruise trim speed. If it requires a still greater ‘‘pull’’ force to maintain this lower airspeed, the aircraft has POSITIVE STATIC LONGITUDINAL STABILITY. If at either test points, no ‘‘pull’’ force is required to maintain the reduced airspeeds, the aircraft has NEUTRAL STATIC LONGITUDINAL STABILITY. If either of these test points require a ‘‘push’’ force to maintain the reduced air-speed then the aircraft has NEGATIVE STATIC LONGITUDINAL STABILITY. |  |
| 8 | Repeat another series of static longitudinal stability tests Use a ‘‘push’’ force on the control stick At an airspeed 10 percent above the trim cruise speed the control stick should require a ‘‘push’’ force to maintain the airspeed. If a ‘‘pull’’ force is required, the aircraft has NEGATIVE STATIC LONGITUDINAL STABILITY. WARNING: If the aircraft exhibits negative static longitudinal stability, seek professional advice on correcting the problem before further flight. |  |
| 9 | Check for positive DYNAMIC longitudinal stability Trim the aircraft to fly straight and level at normal trim cruise speed. With a smooth, but fairly rapid motion, push the nose down a few degrees. Quickly reverse the input to nose up to bring the pitch attitude back to trim attitude. As the pitch attitude reaches trim attitude, release the stick (but guard it). The aircraft with positive dynamic longitudinal stability will oscillate briefly about the trim attitude before stopping at the trim attitude position Pull (or push) the stick to a speed about 5 knots off trim and release the stick. An aircraft with ‘‘NEUTRAL’’ dynamic longitudinal stability (long period) will continue to oscillate through a series of increasing/decreasing airspeeds and never return to the original trim airspeed. |  |
| 10 | Perform a carbon monoxide (CO) test using an industrial CO test meter |  |
| 11 | Radio Call All stations Caboolture, this is BushCaddy 3670 joining crosswind runway _______________ |  |
| 12 | Radio Call All stations Caboolture, this is BushCaddy 3670, base runway _______________, full stop |  |
| 13 | Taxi to hanger and carryout a complete inspection of the aircraft |  |

### Comments: